## Slide 1: ENERGY FUNDAMENTALS & APPLICATIONS Lecture 1
INTRODUCTION & PRELIMINARIES
Intellectual property of Calvin M. Wolff and is to be used only by permission: calvin@cmwolff.com

## Slide 2: COURSE OBJECTIVE
To provide a thorough and well substantiated understanding of the nature, sources, technology, distribution and economics of energy.

## Slide 3: COURSE OBJECTIVES - Detailed
Learn the basic scientific principles of
  Chemistry
  Mechanics
  Thermodynamics
  Thermochemistry
  Inefficiencies
  Electro-magnetism
  Electric Power
  Light
  Heat Transfer
  Fluid Flow
To understand
  Wind Turbines
  Solar Cells
  Hydroelectric Power
  Lighting
  Air Conditioning
  Auto & Diesel Engines
  Steam Engines
  Jet Engines
  Electric Generators
  Electric Motors
  Electric Power Generation, Transmission & Distribution
Learn the economics of energy

## Slide 4: COURSE CONDUCT
Save Questions Until End of Lesson – there is a lot of material and time is critical
Some numerical problems
Comments are Welcome after/before Class and via e-mail
I’ll make time for you.

## Slide 5: MACRO ENERGY UNITS
U.S. Energy Information Administration (EIA)
  BTU = (British Thermal Unit) heat required to raise temperature of one pound water one degree Fahrenheit
(Calorie = heat required to raise temperature of one gram water one degree Celsius) 1 calorie = 4.186 joules =
  Quad = One Quadrillion (1015) BTU’s 1 barrel of oil has 5.8 Million BTU’s, at $50/bbl one Quad of Oil is Worth $8.6 Billion;
    1 MMBTU Natural Gas is worth $3, 1 Quad Natural Gas is Worth about $3 Billion
Global Energy Statistics: Reserves & Resources (used in Text)
  Exajoule (EJ) = 1015 Kilojoules = 957 Quads

## Slide 6: ENERGY RESOURCES & RESERVES
RESOURCE is the estimated global natural occurrence of a particular form of matter or energy
RESERVE is the subset of the resource that is available for exploitation today
  Relatively precise knowledge of location & magnitude
  Technological capability to extract and process deposits
  Projected cost of production that is below or near current market prices

## Slide 7: SUMMARY OF GLOBAL FOSSIL FUEL ESTIMATES
(Excludes Methane Hydrates) |  |  | 
 | As of Year 2000 in Exajoules |  | 
FUEL | Reserves | Resource | Estim. Years*
Coal | 21,000 | 200,000 | <400
Conventional Oil | 6,000 | 12,000 | <150 combined
Unconventional Oil | 5,000 | 20,000 | 
Conventional Nat Gas | 5,500 | 16,500 | <300 combined
Unconventional Nat Gas | 9,500 | 33,000 | 
Total Fossil | 47,000 | 281,500 | 
Uranium, non-Breeder | 1,900 | 8,500 | 47
Uranium, Breeder | Very Large | Very Large | Very Long

## Slide 8: ENERGY SOURCES
FUNDAMENTAL: Nuclear & Gravity
PRIMARY
  Fossil: Coal, Oil, Oil Shale, Oil Sand, Nat. Gas, Methane Hydrates
  Nuclear: Fusion & Fission - Breeder & Non-Breeder
  Renewable: Solar, Wind, Hydro (e.g. Dams), Geothermal, Biomass
  Efficiency
SECONDARY
  Electric Power: Economic, Easily Distributed, Envionmentally Manageable
  Steam: Useful, Difficult to Distribute, Moderate Energy Density
  Refined and Bio-Fuels: High Energy Density, Portable, Easy to Store
  Hydrogen: Difficult to Distribute and Store

## Slide 9: ENERGY DENSITIES

## Slide 10
ENERGY DENSITIES |  |  |  |  | 
 | BY MASS |  |  | BY VOLUME | 
 | MJ/Kg | BTU/lb | Relative to Gasoline | MJ/L | Relative to Gasoline
Solar Fusion | 6.40E+07 | 2.75E+10 | 1,379,310 |  | 
235U Fission | 6.45E+06 | 2.78E+09 | 139,009 | 1.50E+09 | 4.39E+07
Li Ion Battery | 2.6 | 1,119 | 0.06 | 1.2 | 0.04
H2 Fuel Cell | 1.6 | 689 | 0.03 |  | 
Lead Acid Battery | 0.1 | 43 | 0.00 |  | 
Liq. Hydrogen | 143 | 61,537 | 3.08 | 10.1 | 0.30
Flywheel | 0.5 | 215 | 0.01 |  | 
Ni-Cad Battery | 0.18 | 77 | 0.00 |  | 
Compr. H2, 10,000 psi | 143 | 61,537 | 3.08 | 5.6 | 0.16
Natural Gas | 53.64 | 23,083 | 1.16 | 10.0 | 0.29
Bio Diesel | 42.2 | 18,160 | 0.91 | 33.0 | 0.96
Crude Oil | 46.3 | 19,924 | 1.00 | 37.0 | 1.08
Propane | 49.5 | 21,301 | 1.07 | 25.3 | 0.74
Diesel | 46.2 | 19,881 | 1.00 | 37.3 | 1.09
Gasoline | 46.4 | 19,967 | 1.00 | 34.2 | 1.00
Body Fat, Metabolized | 38 | 16,353 | 0.82 | 35.0 | 1.02
Anthracite Coal | 32.5 | 13,986 | 0.70 | 72.4 | 2.12
Ethanol | 30 | 12,910 | 0.65 | 24.0 | 0.70
Bituminous Coal | 24 | 10,328 | 0.52 | 20.0 | 0.58
Sugars, Carbohydrates | 17 | 7,316 | 0.37 | 26.2 | 0.77
Wood | 10 | 4,303 | 0.22 |  | 
Household Waste | 9 | 3,873 | 0.19 |  | 

## Slide 11: ENERGY USAGE
Transportation
Lighting
HVAC (Heating, Ventilation, Air Conditioning)
Motors
Industrial Process Energy
Industrial Process Feedstocks

## Slide 12: NATURAL GAS & CRUDE PRICES
Go to http://www.nymex.com/
Click “Crude Oil (CL)” or Natural Gas (NG)” – an agreement page will come up
Click “I Accept”
Click “Current Expanded Table” from menu on left, goes out about 8 years.
Contracts are for 1,000 bbl (oil) and 10,000 MMBTU (nat. gas)

## Slide 13: Sources of Energy Information
International Energy Agency fact sheets http://www.worldenergyoutlook.org/media/weowebsite/2015/WEO2015_Factsheets.pdf
BP World Statistical Review of World Energy http://www.bp.com/content/dam/bp/excel/energy-economics/statistical-review-2016/bp-statistical-review-of-world-energy-2016-workbook.xlsx

## Slide 14: WORLD ENERGY PRODUCTION
Fuel Type | Production, Mtoe*
Petroleum | 4331.2
Natural Gas | 3135.2
Coal | 3839.9
Nuclear | 583.1
Hydroelectric | 892.9
Renewables | 364.9
TOTAL 1347.3
*Mtoe = Million Tons Oil Equivalent = 3.96E13 BTU = 0.0396 Quads

## Slide 15: BP Statistical Review Contents
Oil: Proved reserves
Oil: Proved reserves - Barrels (from 1980)
Oil: Production – Barrels (from 1965)
Oil: Production – Tonnes (from 1965)
Oil: Consumption – Barrels (from 1965)
Oil: Consumption – Tonnes (from 1965)
Oil: Regional consumption – by product (from 1965)
Oil: Spot crude prices
Oil: Crude prices since 1861
Oil: Refinery throughput (from 1980)
Oil: Refinery capacities (from 1965)
Oil: Regional refining margins (from 1992)
Oil: Trade movements (from 1980)
Oil: Inter-area movements
Oil: Trade 2014-2015
Coal: Reserves
Coal: Prices
Coal: Production - Tonnes (from 1981)
Coal: Production - Mtoe (from 1981)
Coal: Consumption - Mtoe (from 1965)
Nuclear Energy – Consumption - TWh (from 1965)
Nuclear Energy – Consumption - Mtoe (from 1965)
Hydroelectricity – Consumption - TWh (from 1965)
Hydroelectricity – Consumption - Mtoe (from 1965)

## Slide 16: BP Statistical Review Cont’d
Gas: Proved reserves
Gas: Proved reserves - Bcm (from 1980)
Gas: Production – Bcm (from 1970)
Gas: Production – Bcf (from 1970)
Gas: Production – Mtoe (from 1970)
Gas: Consumption – Bcm (from 1965)
Gas: Consumption – Bcf (from 1965)
Gas: Consumption – Mtoe (from 1965)
Gas: Trade movements pipeline
Gas: Trade movements LNG
Gas: Trade 2014-2015
Gas: Prices
Renewables - Other renewables consumption -Twh (from 1965)
Renewables - Other renewables consumption - Mtoe (from 1965)
Renewables - Solar consumption - TWh (from 1965)
Renewables - Solar consumption - Mtoe (from 1965)
Renewables - Wind consumption - TWh (from 1965)
Renewables - Wind consumption - Mtoe (from 1965)
Renewables - Geothermal, Biomass and Other - TWh (from 1965)
Renewables - Geothermal, Biomass and Other - Mtoe (from 1965)
Renewables - Biofuels production - Kboe/d (from 1990)
Renewables - Biofuels production - Ktoe (from 1990)

## Slide 17: BP Statistical Review, Concl’d
Primary Energy: Consumption - Mtoe (from 1965)
Primary Energy: Consumption by fuel type - Mtoe (2014-2015)
Electricity Generation - TWh (from 1985)
Carbon Dioxide Emissions (from 1965)
Renewable Energy - Geothermal (Installed capacity)
Renewable Energy - Solar (Installed capacity)
Renewable Energy - Wind (Installed capacity)
Approximate conversion factors
Definitions

## Slide 18: U.S.A. ENERGY FLOW
Units are Quads

## Slide 19: WORLD ENERGY FLOW
Petroleum
Nat. Gas
Coal
Electricity & Heat
Biomass
Nuclear
Hydro
Elec.
Residential
Commercial
Transportation
Industrial
Rejected Energy
Useful Energy
Heat

## Slide 20: LET’S GET TECHNICAL

## Slide 21: Decimal Prefixes
Nano | 1 billionth | E-9, E-09
Micro | 1 millionth | E-6, E-06
Milli | 1 thousandth | E-3, E-03
Centi | 1 hundredth | E-2, E-02
Deci | 1 tenth | E-1, E-01
Deca | ten | E1, E01
Hecta | hundred | E2, E02
Kilo | thousand | E3, E03
Mega | million | E6, E06
Giga | billion | E9, E09
Tera | trillion | E12
Peta | quadrillion | E15
Exa | pentillion | E18

## Slide 22: Mathematical Notation
Unit^n = Unitn, example cm^3 = cm3 = cubic centimeter
En = 10n; examples for n-2: 4.5E-2 = 4.5 x 10-2 = 0.045 E9 = E09 = 1E9 = 1 billion
Dot over a variable = time rate of change of the variable, example: the time rate of change of velocity is acceleration v = a
Differentials (difference between two values):
Xa – Xb = ΔX for finite differentials = δx for small finite differentials
= dX for infinitesimally small differentials
Angles are symbolized by θ and φ , and are generated according to right-hand-rule; i.e., x to y, y to z, and z to x.
The sum of finite differentials (ΔX) is signified by Σ ΔX
The sum of infinitesimally small differentials (dx) is signified by the integral ∫ dx
Ordinary multiplication operator is “ * ” ; as 2 * 2 = 4

## Slide 23: DEFINITIONS - 1
Matter – anything that occupies space and has mass
Mass – how much matter there is in an object, resists acceleration
Scalar - a mathematical entity representing quantity only
Vector – a mathematical entity that has scalar value and direction
Speed – scalar time rate of motion, units of length per unit time
Velocity – a vector: speed and direction
Acceleration – a vector whose scalar value is the rate of change of speed, units of length/(time) 2 or l / t2
Force – a vector causing or resisting acceleration of a body with mass
Gravity – acceleration caused by mass, l / t2
Weight – force of gravity on mass ml / t2
Torque – a vector representing the tendency of a force to rotate an object about some axis m l2 / t2
Pressure – a scalar, the force per unit area applied to an object in a direction perpendicular to the surface. (pressure within a closed volume is the same in all directions) m / l t2 or or m l-1t-2
Work – a scalar physical entity equal to a force moving a mass through a distance parallel to the force m l2 / t2 or m l2 t-2

## Slide 24: DEFINITIONS - 2
Energy - a property of objects which can be transferred to other objects or converted into different forms, but cannot be created or destroyed.
Energy – also defined as a scalar physical entity representing the ability to do work
Power – amount of energy transferred or work done per unit of time.

## Slide 25: Dimensional Analysis
Every physical entity (mass, velocity, energy, etc.) has specific dimensions
“m” for mass, “l” for length or distance, “t” for time, “T” for temperature, “q” for electric charge, “$” for cost or value.
Area l 2
Volume l 3
Velocity: l /t
Acceleration l /t2
Momentum m l /t mass x velocity
Force m l /t2 mass x acceleration
Pressure m/ l t2 force / area or force per unit area
Energy, work, torque m l 2/t2 as work, force x distance traversed
Density m/ l 3 mass per unit volume
Heat Capacity l 2/t2T change in heat energy per change in unit temperature per unit mass
Power m l 2/t3 energy per unit of time
Current q/t charge per unit of time
Voltage m l /t2q energy per unit charge
Electric rate $t2 / m l 2 cost per unit of electrical energy (KWh)

## Slide 26: TYPICAL UNITS
Mass: grams, Kg, lb, oz, mg
Length: meters, cm, mm, inch, foot, yard
Time: seconds, minutes, hours
Temperature: deg F, deg C, deg K, deg R
Electric Charge: coulomb
Value: dollar

## Slide 27: SYSTEMS OF UNITS
cgs = centimeter-gram-second
mks = meter-kilogram-second (SI system)
English = ft, lbm (pound mass), lbf (pound force), BTU, second & hour

## Slide 28: CONVERSION FACTORS – by System
UNIT | MKS | CGS | ENGLISH
Length | meter | 10^2 cm | 3.288 feet
Area | sq. meter | 10^4 cm2 | 10.81 ft^2
Volume | cubic meter | 10^6 cm3 = 1,000,000 ml | 35.31 ft^3
Mass | kilogram | 1000 grams | 2.203 lbm
Density | Kilogram/meter^3 | 0.001 g/ml | 0.0624 lbm/ft^3
Velocity | meters /sec | 100 cm/sec | 3.288 ft/sec
Acceleration | meters/sec^2 | 100 cm/sec^2 | 3.288 ft/sec^2
Force | newton, kg-m/sec^2 | 10^5 dynes (gm-cm/sec^2) | 0.225 lbf
Pressure | pascal, newton / m^2 | 10 dyne/cm^2 (baryes) | 0.000145 psi
Energy | joule (newton-meter) | 10^7 ergs, (dyne-cm) | 0.000957 BTU
Energy | Kilojoule | 10^10 ergs | 0.957 BTU
Energy | watt-hour |  | 3.443 BTU
Power | watt (joule / sec) |  | 1.34 HP
Temperature | degree Celsius or Kelvin |  | 1.8 deg Fahrenheit or Rankine
Enthalpy | joule/g = Kjoule/Kg |  | 0.43 BTU/lbm
Entropy | joule/Kg-degK |  | 0.239 BTU/lbm-degR
Heat Capacity | joule/Kg-degK |  | 0.239 BTU/lbm-degR

## Slide 29: More Useful Conversion Factors
1 lbm = 454 grams = 0.454 Kg
1 liter = 1E-3 cubic meters = 0.264 gallons
1 HP = 0.746 KW = 550 ft-lbf/sec = 33,000 ft-lbf/sec
1 micron = 1E-6 meter
1 BTU = 778 ft-lbf = 1,055 joules = 1.055 Kj
1 KPa (KiloPaschal pressure) = 0.145 lbf/in^2 (psi)
1 electron volt (eV) = 1.602E-19 Joules
1 lbf = 4.448 Newtons
1 Quad = E15 BTUs
1 Mtoe (Megatons oil equivalent) = 3.96E13 BTU
1 Metric Ton = 1 Tonne = 1,000 Kg = 2,200 lb